## Slide 1
ARCHITECTURE EVOLUTION & PLATFORM MODIFICATIONS
Environment-Agnostic Perception Platform
Standardized Core Perception Engine, Human-in-the-Loop Bootstrap & Autonomous Edge Auditing
This presentation details the architectural refactoring of the SITE Assets Monitor system. We have transitioned the perception stack from an environment-dependent prototype into a modular, configuration-driven base platform capable of rapid multi-client deployment with zero core code changes, seamless Human-in-the-Loop onboarding, and optimized CPU execution on mobile ground robots.
CORE ARCHITECTURE
3-Tier Layered Framework
Frozen Engine + Profile + Rules
HARDWARE BOUNDARY
Raspberry Pi 5 (CPU)
Zero Onboard Training Required
DEPLOYMENT VELOCITY
< 1 Day Calibration
Zero Per-Client Code Rewrites
SITE Assets Monitor | Environment-Agnostic Perception Platform Architecture
1 / 10

## Slide 2
STRATEGIC MOTIVATION
Why Evolve from a Prototype to a Scalable Platform?
Moving from brittle, site-specific code to an industrial base engine designed for fleet scale.
BEFORE: Site-Specific Prototype
Tightly coupled to a single environment and fixed taxonomy.
• Hardcoded Rules & Classes:
Model classes, camera settings, and thresholds were hardcoded in Python files.
• Expensive Per-Client Engineering:
Deploying to a second client (e.g. port or warehouse) required branching code and rewriting logic.
• No Adaptation Mechanism:
If lighting shifted or new machinery arrived, the system had no structured way to learn or adjust.
• High Maintenance Overhead:
Bug fixes in one deployment could not be easily pushed to other client sites without merging conflicts.
NOW: Environment-Agnostic Platform
Modular, profile-driven engine deployable anywhere in hours.
✔ Zero Code Changes per Site:
100% of site-specific behavior is configured in clean YAML profiles.
✔ Unified Core Engine:
Base perception algorithms (quality filtering, detection, ReID, spatial tracking) remain standard and frozen.
✔ Rapid HITL Calibration:
Built-in Human-in-the-Loop workflow collects on-site data Day 1 and bootstraps autonomous tracking.
✔ Continuous Fleet Updates:
Core algorithmic enhancements can be deployed universally to all client robots with zero site breakage.
SITE Assets Monitor | Environment-Agnostic Perception Platform Architecture
2 / 10

## Slide 3
SYSTEM ARCHITECTURE
The 3-Tier Layered Architecture
Strict separation between standard vision algorithms, site parameters, and use-case rules.
TIER 1
Standard Base Engine
Status: 100% Reusable (Frozen)
The core algorithmic perception foundation. Identical on every robot and client site.
CORE MODULES & DUTIES:
• Image Quality Checker (Rejects motion blur & bad lighting)
• YOLOv8 Neural Detector (ONNX Edge Inference)
• OSNet Deep Visual Re-ID (512D spatial embeddings)
• Reference Store (Cosine similarity & multi-view centroids)
• Forensic Evidence Generator (Raw frames + annotated crops + JSON metadata)
TIER 2
Deployment Profiles
Status: Config Only (YAML)
Site-specific settings injected at startup. Enables new client setup in under an hour.
CORE MODULES & DUTIES:
• Hardware Mapping (Camera resolution, FPS, ROS2 topics)
• Site Asset Taxonomy (Target machinery classes & priorities)
• Quality Gate Thresholds (Tolerances for outdoor vs indoor light)
• Model Weights Pointer (Path to site-calibrated ONNX model)
• Storage Paths (Evidence directories and retention policies)
TIER 3
Use-Case Rules Layer
Status: Client Business Logic
High-level rules that translate raw perception states into operational security actions.
CORE MODULES & DUTIES:
• Movement Geofencing (e.g. 3-meter displacement violation)
• Missing Equipment Alerting (Temporal hysteresis buffer)
• Shift Audit Generator (Shift-end asset compliance report)
• ROS2 / Webhook Event Dispatcher (Security operator alerts)
SITE Assets Monitor | Environment-Agnostic Perception Platform Architecture
3 / 10

## Slide 4
OPERATIONAL LIFECYCLE
The 5-Phase Deployment Lifecycle
Step-by-step path from unboxing the robot on Day 1 to fully autonomous 24/7 site auditing.
PHASE 0
Pre-Deployment
~1-2 Hours (Engineering)
• Clone base software repo on robot.
• Create 'profiles/client.yaml' from template.
• Configure camera, ROS2 topics, & FPS.
• Zero algorithmic code modification.
PHASE 1
HITL Bootstrap
Day 1 (2-4 Hours On-Site)
• Robot patrols site guided by operator.
• Camera captures equipment crops.
• Operator confirms/names assets on tablet.
• Builds initial Re-ID visual fingerprints.
PHASE 2
Offline Tuning
~30 Min (Laptop / Cloud)
• Transfer Day 1 photos to engineer's laptop.
• Run transfer learning fine-tuning on GPU.
• Export single lightweight ONNX model file.
• Copy ONNX to Pi 5 & point YAML to it.
PHASE 3
Autonomous Ops
Day 2 Onwards (24/7)
• Robot audits assets completely marker-free.
• Real-time 3-5 FPS inspection on Pi 5 CPU.
• Evaluates location, movement, & status.
• Auto-generates legal-grade evidence packages.
PHASE 4
Gradual Handoff
Weeks 1 to 4 (The HITL Dial)
• Week 1: ~50% human review (new assets).
• Week 2: ~20% review as library expands.
• Week 4+: <5% review (rare anomalies only).
• Near-zero routine human supervision.
SITE Assets Monitor | Environment-Agnostic Perception Platform Architecture
4 / 10

## Slide 5
COMPUTE ARCHITECTURE
Edge Execution vs Offline Fine-Tuning Clarified
How we achieve high accuracy on low-cost robot hardware without expensive onboard GPUs.
ON THE ROBOT: Raspberry Pi 5 (Edge CPU)
Dedicated solely to live inference and evidence logging.
✔ Inference Only (No Onboard Training):
The Pi 5 has no NVIDIA CUDA GPU. Training on a Pi 5 would overheat, freeze RAM, and take days. It only *runs* pre-optimized models.
✔ Fast ONNX CPU Runtime:
Executes pre-compiled ONNX models at ~250-350ms per inspection cycle, delivering an optimal 3-5 FPS for slow-moving ground AMRs.
✔ Low Power & Cost:
Operates under 15 Watts without draining robot patrol battery life or requiring costly $2,000+ industrial GPU computers.
✔ Day 1 Data Collector:
During Phase 1, the Pi 5 acts as a high-fidelity image recorder, capturing real-world crops for offline training.
OFFLINE: Laptop / Cloud GPU (Fine-Tuning)
The 30-minute transfer learning step on an engineer's GPU.
⚡ Where Training Happens:
Executed on an engineer's laptop with an NVIDIA RTX GPU or a free cloud notebook (Google Colab).
⚡ Transfer Learning Speed:
Base model weights are kept frozen; only the final classification layer is adapted. Takes only 20-30 minutes for 200-500 images.
⚡ One-Step ONNX Export:
A single command converts the trained model into a portable '.onnx' binary (~12MB), optimized for CPU math.
⚡ 1-Minute File Drop Deployment:
Copy the '.onnx' file to the robot via Wi-Fi or USB drive, update 1 line in 'detection_config.yaml', and restart. Zero code edits.
SITE Assets Monitor | Environment-Agnostic Perception Platform Architecture
5 / 10

## Slide 6
LIVE RUNTIME INTELLIGENCE
Live Inference Pipeline & 4-Tier Identity Verification
How each camera frame is evaluated in real time to guarantee accuracy and eliminate false alarms.
Frame Processing Pipeline (Every 200-300ms)
▶ 1. Quality Gate
Rejects blurry, overexposed, or pitch-black frames in ~2ms before deep models run.
▶ 2. YOLOv8 Detection
Detects machinery bboxes and initial class categories in ~150-180ms.
▶ 3. Deep Re-ID Fingerprint
OSNet extracts a 512-dimensional visual embedding vector from valid crops (~60ms).
▶ 4. Spatial Reference Match
Calculates cosine similarity against stored asset fingerprints in the ReferenceStore (~1ms).
▶ 5. Spatial Delta Tracking
Compares detected position with baseline. Computes displacement vs 3m threshold.
▶ 6. Evidence & ROS2 Publish
On state change or violation, logs raw + annotated evidence and publishes to ROS2 topic.
4-Tier Identity Confidence System
● CONFIRMED — Similarity ≥ 0.85 (High Margin)
Action: Definite match. Asset identity is locked. State updated in registry without operator distraction.
● PROBABLE — Similarity ≥ 0.65
Action: Match under non-ideal angles or lighting. Logged with audit flag; automated tracking continues.
● AMBIGUOUS — Two Assets Competing Closely
Action: Cosine scores are tied (margin < 0.15). Alerts operator tablet for quick validation instead of guessing.
● UNKNOWN — Similarity < 0.40
Action: New equipment arrived on site. Auto-registers as candidate asset or triggers security onboarding review.
SITE Assets Monitor | Environment-Agnostic Perception Platform Architecture
6 / 10

## Slide 7
ROBUSTNESS & RELIABILITY
Built for Industrial Field Conditions
Proactive engineering safeguards addressing lighting variations, occlusions, and compute limits.
01 | Lighting & Sun Shadow Shifts
Challenge: Harsh morning vs late afternoon sunlight alters machine appearance.
Safeguard: Multi-Embedding Centroids: The ReferenceStore stores up to 10 visual embeddings per asset across different times of day, computing a stable mathematical centroid resistant to glare and shadows.
02 | Temporary Obstacles & Occlusion
Challenge: A passing truck or worker momentarily blocks the camera's view.
Safeguard: Temporal Hysteresis Buffering: Missing alerts are NEVER raised on a single frame dropout. The system requires N consecutive patrol misses before flagging 'ASSET MISSING', eliminating false security calls.
03 | Pi 5 Compute Bottlenecks
Challenge: Multiple machines in frame could drop frame rate below target.
Safeguard: Adaptive Re-ID Execution: If an asset's bounding box is stationary across consecutive frames, deep Re-ID embedding extraction is safely bypassed, preserving steady 3-5 FPS execution.
04 | Forensic-Grade Evidence Logging
Challenge: Disputed relocation events or auditing compliance challenges.
Safeguard: Dual-Stream Cryptographic Evidence: Saves pristine unannotated original frames, cropped asset views, annotated overlays, and JSON metadata with robot coordinates and timestamps for legal compliance.
SITE Assets Monitor | Environment-Agnostic Perception Platform Architecture
7 / 10

## Slide 8
EXECUTIVE BUSINESS CASE
Commercial & Operational Impact
Comparing project velocity, deployment costs, and operational reliability.
CLIENT DEPLOYMENT SPEED
Prototype: 2–3 Weeks of Custom Engineering ➔ Agnostic Platform: < 1 Day Calibration (Profile + HITL)
Business Value: 90% faster rollout. Enables signing and onboarding new facilities without software bottlenecks.
CODEBASE MAINTAINABILITY
Prototype: Fragmented Forks per Client Site ➔ Agnostic Platform: Single Unified Base Codebase
Business Value: One bug fix or vision enhancement benefits every deployed robot simultaneously.
VISUAL ACCURACY & RELIABILITY
Prototype: Generic Out-of-the-Box Models (~50-60%) ➔ Agnostic Platform: Environment-Calibrated ONNX (85-95%+)
Business Value: Near-zero false alarms; high operator trust from day two of deployment.
HARDWARE INVESTMENT
Prototype: High-Cost Industrial GPU Modules ➔ Agnostic Platform: Low-Power Raspberry Pi 5 CPU
Business Value: Keeps robot build costs low while ensuring 24/7 battery endurance on mobile patrols.
SITE Assets Monitor | Environment-Agnostic Perception Platform Architecture
8 / 10

## Slide 9
EXECUTION ROADMAP
Milestones & Immediate Next Steps
Structured technical roadmap leading to live client demonstration and field validation.
STAGE 1
Modular Profile Loader
Status: In Progress (Current Sprint)
KEY DELIVERABLES:
✔ Implement 'profile_loader.py' to parse YAML into active runtime modules.
✔ Inject dynamic class taxonomies & confidence thresholds.
✔ Ensure zero hardcoded paths across 'detector.py' and 'reference_store.py'.
STAGE 2
ROS2 Navigation Handshake
Status: Awaiting Bag File / Topics
KEY DELIVERABLES:
✔ Map 2D camera pixels to 3D site coordinates via map projection.
✔ Subscribe to camera frame topic and robot pose/TF topics.
✔ Publish verified asset detections to '/perception/detections'.
STAGE 3
HITL Capture & Field Pilot
Status: Pilot Validation
KEY DELIVERABLES:
✔ Deploy tablet-friendly HITL calibration interface for site walkthrough.
✔ Run 30-min offline fine-tuning workflow on captured assets.
✔ Conduct full 24-hour autonomous audit trial at client facility.
SITE Assets Monitor | Environment-Agnostic Perception Platform Architecture
9 / 10

## Slide 10
SITE Assets Monitor
Ready to Power Multi-Site Autonomous Auditing & Visual Security
ZERO CODE REWRITES
Profile-Driven Flexibility
• 100% config-based onboarding.
• Deploy to construction sites, ports, or warehouses using YAML profiles.
• Central core engine remains untouched and scalable across all clients.
EDGE-OPTIMIZED EFFICIENCY
Raspberry Pi 5 Ready
• Smooth 3-5 FPS inference on low-power onboard CPU.
• Zero heavy onboard GPU requirement.
• Offline 30-min fine-tuning yields high-accuracy custom ONNX weights.
HIGH-CONFIDENCE AUDITING
Autonomous Security & Audits
• Markerless visual Re-ID with 4-tier confidence verification.
• Defensible dual-stream evidence generation with tamper-proof metadata.
• Seamless integration with mobile robot ROS2 navigation stacks.
SITE Assets Monitor | Environment-Agnostic Perception Platform Architecture
10 / 10